## Slide 1: Drone Recovery Robot
Matt Kennedy
John Furumo
Snapshot of Robot Model
from RoboWorks

## Slide 2
9-DEC-2019
ENAE692/Robot Project
2
Robotic Task (Description)
Notes: 2

## Slide 3
Kinematic Requirements
  Have a large horizontal and vertical reach
  Be able to track a target in space with quickly changing conditions (wave motion, flight controls)
Workspace Requirements
  Reach into safe flight path away from ship
  Match orientation of drone
Force Requirements
  Impact with 6kg drone moving at ~40km/h
Other
  Return drone to ship deck
  Stow arm safely on-board ship
9-DEC-2019
ENAE692/Robot Project
3
Robotic Task (Requirements)

## Slide 4: Robot Design (Specifications)
Description | Specification
Total Degrees of Freedom | 7
Arm Type* | DYPDPRY
Wrist Type† | PRY (IAW-No)
Redundancy | elbow orbit angle
Length Sum (L) | 10.4 m
Structural Length Index (Q) | 0.62
*R=roll, P=pitch, Y=yaw, D=prismatic
†IAW-intersecting axis wrist

## Slide 5: Robot Design (Link Frames)
x0
z0
x1,x2
z1, z2, x3
z3
d1
d4
z4
x4,x5
z5
z6
z7
x6,x7
Q2
Q3
Q5
Q6
Q7
tern device
Side View
x1,x2
z1, z2, x3
z3
d4
z4
z5
x4
z6
z7
x6,x7
Q3
Q2
Q5
Q6
Q7
Top View
qHOME=[2.5m, 0 rad, p/2 rad, 2.5m, 0, 0, 0]T
a4
x5
a3

## Slide 6: Robot Design (D-H Table)
i | ai-1 (deg) | ai-1 (m) | di (m) | qi (deg) | JL- (deg) | JL+ (deg)
1 | 0 | 0 | d1 | 0 | 2.5m | 3.75m
2 | 0 | 0 | 0 | Q2 | -180 | 180
3 | 90 | 0 | 0 | Q3 | 45 | 135
4 | 90 | 0.4m | d4 | 0 | 2.5m | 3.75m
5 | -90 | 0.75m | 0 | Q5 | -45 | 45
6 | 90 | 0 | 0 | Q6 | -22.5 | 22.5
7 | 90 | 0 | 0 | Q7 | -45 | 225
JL = JOINT LIMIT

## Slide 7: Robot Design (Joint Animation)
My Awesome Robot
(Show the motion of each joint in RoboWorks)

## Slide 8
9-DEC-2019
ENAE692/Robot Project
8
Forward Kinematics

## Slide 9
q = [50,1.92,1.57,50,0,0,-1.92]
  p0T=
  R0T=
q = [50,0,1.57,50,0,0,0]
  p0T=
  R0T=
  q = [50.8,1.57,1.75,50.85,-0.18,0,-1.57]
  p0T=
  R0T=
snapshot
9-DEC-2019
ENAE692/Robot Project
9
Forward Kinematics (Test)
Notes: 9

## Slide 10: Inverse Kinematics (Solution)

## Slide 11
Inverse Kinematics (Test)
qSTART = [50,0,pi/2,50,0,0,0]
0pGOAL= [65,65,65],
0RGOAL= [pi/8,-pi/8,0]=[yaw,pitch,roll]
show start configuration
Solution:
QGOAL = [50.84,0.32,2.09,72.63,-0.52,-0.39,0.077]
Solution Check:
0pT (qGOAL) = [65,65,65]
show end configuration
9-DEC-2019
ENAE692/Robot Project
11

## Slide 12: Translational Jacobian (Base Frame)

## Slide 13: Rotational Jacobian (Base Frame)

## Slide 14
Internal:
Boundary:
linearly dependent columns
9-DEC-2019
ENAE692/Robot Project
14
Singularities

## Slide 15
Maximum Task Force/Torque:
FMAX = [0, 300N, 0], NMAX = [0,0,0]
Workspace Pose:
Joint Position:
qT= [50.77,1.57,1.75,50.84,-0.18,0,-1.57]

 = J*F=[0,-15000,-6369,295,
-3600,15000,15000]
(Joint Torques)
9-DEC-2019
ENAE692/Robot Project
15
Force
Maximum Load

## Slide 16: Task (Animation)
Task Animation
(Show task execution in RoboWorks)
*Note: required for teams of 2

## Slide 17: Conclusions
Robot Design
  The workspace is adequate for the task in question
  Singularities do not provide a major obstacle to overcome
  Kinematic Redundancy
Future Work
  Add stabilization of boat motion to dynamics
  Other applications – land use
What I Learned
  More DoF not always advantageous
  Difficult to model and visualize kinematics beyond minimal DoF

## Slide 18: Back-up

## Slide 20
Drone Recovery Arm
Robot Design:
Initial concept uses 5 revolute joints for positioning and orientation, and a prismatic joint near the base for additional stabilization.
The estimated required arms lengths are:
D2 = 2-3m
L3 = 1m
L4 = 1m
Though design requirements will be further investigated for optimal workspace to ensure safe wave-offs. The end-effector catching mechanism is initially proposed to be a simple net, though the effectiveness of others will be investigated.
Team: Matt Kennedy
John Furumo
Drone Recovery Arm mounted to LCS Flight Deck
Objective:
Design a manipulator capable of safely recovering both fixed wing and rotary drones to an underway ship.
Motivation:
• Facilitate drone recovery in all weather
• Facilitate drone recovery to all ship types
Task Requirements:
Kinematics
  3 DOF to orient the catching mechanism
  3 DOF to adjust height and stabilize tool tip
Workspace
  Orient catching mechanism to 1m (width) by 2m (height) target area
  Lower catching mechanism to ground for drone removal
Force/Moment
  Impact with 40kg drone moving 10m/s (for fixed wing)
23-OCT-2019
Notes: 20